## Slide 1
NIT
JSR
NATIONAL INSTITUTE OF TECHNOLOGY JAMSHEDPUR
Department of Mechanical Engineering
Intelligent Bearing
Fault Diagnosis
for Predictive Maintenance
Project-II | CM1611
SUBMITTED BY
Pradeep Modak
2023UGCM026
Ashwini Kumar
2023UGCM004
SUPERVISED BY
Dr. Saroj Sarangi
Dr. Abhijit Dey
Spring Semester 2025-26 • April 2026

## Slide 2
OUTLINE
01
Introduction
02
Applications
03
Literature Survey
04
Research Gaps & Objectives
05
Methodology & Workflow
06
Work In Progress
08 References
22
07 Summary

## Slide 3
INTRODUCTION
Background
The Critical Role of Bearings
Rotating machinery depends heavily on rolling element bearing health. Defects cause:
Excess heat & noise
Efficiency loss
Catastrophic shutdowns
Vibration analysis is the most widely used non-invasive technique for early fault diagnosis.
📊
Time-Domain Analysis
Here we study how vibration amplitude changes with time and extract statistical indicators like RMS, standard deviation, skewness, kurtosis, and crest factor. These features help us capture signal energy, impulsiveness, and abnormal peaks caused by bearing defects.
🔍
Frequency Analysis
We apply FFT to convert the signal from time to frequency space. This reveals dominant frequency components and spectral patterns that are strongly linked to fault types such as inner race, outer race, and ball defects. Frequency features improve separability between classes.
🧠
ML Classification
We combine time- and frequency-domain features into a feature vector and train models like SVM and Random Forest. The classifier learns fault-specific patterns and predicts the bearing condition automatically. This gives us a fast, interpretable, and practical diagnosis pipeline

## Slide 4
INTRODUCTION: Problem Statement
THE DIAGNOSTIC CHALLENGE
Manual interpretation of vibration signals is time-consuming and demands extreme domain expertise. Large volumes of continuous sensor data make manual analysis completely unscalable for modern industrial facilities a single plant may generate terabytes of vibration data daily.
🎯 PROJECT FOCUS
Build a reliable, interpretable, and automated end-to-end ML pipeline that classifies bearing vibration signals into:
Normal
Ball Fault
Inner Race Fault
Outer Race Fault
Dataset: CWRU Benchmark • 9,736 labeled windows • 48 kHz sampling • 4 bearing conditions

## Slide 5
FUTURISTIC APPLICATIONS
Where this technology transforms industries
🏭
SMART MANUFACTURING
Industry 4.0
Integration with Smart Factories for real-time health scoring across entire production lines. Enables zero-downtime manufacturing.
💨
GREEN ENERGY
Energy Sector
Predictive maintenance for Wind Turbines and Hydroelectric generators, reducing maintenance costs by up to 30%.
🚀
SAFETY CRITICAL
Aerospace
Fault monitoring in jet engine bearings for enhanced passenger safety. Real-time alerts prevent catastrophic failure.
"Shifting from Reactive to Proactive Maintenance Paradigms"

## Slide 6
LITERATURE SURVEY
01
Classical Signal Processing
Waveform analysis, FFT peak identification, wavelet decomposition and fault frequency interpretation.
02
Feature-Based ML
Statistical features extracted + SVM, Random Forest, and gradient boosting classifiers applied.
03
Deep Learning
CNNs and autoencoders learning directly from raw signals or time-frequency images.
KEY RESEARCHERS & BENCHMARK
Kankar et al. (2011)
Demonstrated effectiveness of SVM & Random Forest for bearing classification.
Rajeswari et al. (2014)
Explored Wavelet Packet Transforms combined with hybrid PSO + SVM.
CWRU Benchmark Dataset
The gold standard for evaluating all bearing fault diagnosis methods.

## Slide 7
LITERATURE SURVEY: Limitations
🔒
Hidden Preprocessing
Many studies emphasize model accuracy while keeping all preprocessing and feature engineering assumptions completely opaque making reproduction impossible.
🖥️
Lack of Accessibility
Complete absence of user-facing interfaces for real-time demonstration or educational purposes. Results exist only in research papers.
⚖️
Research-Practice Gap
Prototypes rarely integrate raw signal handling, feature extraction, and GUI deployment in a single cohesive, reproducible workflow.
This project addresses ALL three limitations with a complete, open, end-to-end system.

## Slide 8
RESEARCH GAPS & OBJECTIVES
RESEARCH GAP
Standard literature focuses on model accuracy metrics alone, completely lacking a comprehensive mechanical engineering demonstrative tool that bridges signal processing with web-based inference and interactive visualization.
Missing in existing work:
Full reproducible pipeline
GUI for real-time demos
Explainable feature importance
PROJECT OBJECTIVES
01
Preprocess CWRU signals using 2048-sample windows with 50% overlap
02
Extract 25 engineered time-domain & frequency-domain features
03
Train and compare SVM (RBF) vs. Random Forest classifiers
04
Evaluate with accuracy, precision, recall, and weighted F1-score
05
Deploy an interactive Streamlit Dashboard for live inference

## Slide 9
METHODOLOGY: System Design
1
Data Source
CWRU Bearing
MAT Files
(4 conditions)
→
2
Preprocessing
2048-sample windows
50% overlap
9,736 samples
→
3
Feature Extraction
25 engineered
time + frequency
domain features
→
4
Modeling
SVM (RBF) &
Random Forest
80:20 split
→
5
Deployment
Streamlit Dashboard
Interactive GUI
Live inference
TECHNOLOGIES USED
Python
NumPy / Pandas
SciPy (FFT)
scikit-learn
Matplotlib
Joblib
Streamlit

## Slide 10
METHODOLOGY
Feature
Extraction
Module
⏱ TIME DOMAIN — Statistical Features
Mean & Standard Deviation
Mean Absolute Deviation
RMS (Root Mean Square)
Maximum Absolute Amplitude
Skewness & Kurtosis
Crest Factor, Form Factor
Shape Factor, Impulse Factor
Window: 2048 samples @ 48 kHz = 42.67 ms
〰 FREQUENCY DOMAIN — Spectral Features
FFT Peak Amplitude
Spectral Mean
Spectral Standard Deviation
Dominant Frequency
Spectral Centroid Proxy
Frequency Variance
Frequency Variation Factor
DATASET SUMMARY
9,736
labeled windows
25
engineered features
4
bearing conditions
48 kHz
sampling rate

## Slide 11
RESULTS: Model Performance
97.59%
Random Forest Accuracy
Best Model
97.48%
SVM (RBF) Accuracy
Strong Baseline
Model
Accuracy (%)
Precision (%)
Recall (%)
Weighted F1 (%)
🏆 Random Forest
97.59
97.62
97.59
97.59
SVM (RBF)
97.48
97.50
97.48
97.49
Metric: Accuracy & Weighted F1-Score on held-out 20% test set • Stratified split • Random Forest selected as final deployment model

## Slide 12
RESULTS: Confusion Matrix & Feature Importance
CONFUSION MATRIX — Random Forest
Ball Fault
Ball Fault
Inner Race
Inner Race
Normal
Normal
Outer Race
Outer Race
558
6
0
5
14
606
0
2
1
0
187
0
15
4
0
550
True Label
Predicted Label
TOP FEATURE IMPORTANCES — Random Forest
Spectral Mean
0.158
Impulse Factor
0.098
Std Deviation
0.092
Freq. Variation
0.088
Max Absolute
0.082
RMS
0.075
Mean Abs Dev
0.065
Spectral Std
0.055

## Slide 13
SUMMARY &
CONCLUSION
KEY ACHIEVEMENTS
Integrated mechanical vibration analysis with explainable ML pipeline
Developed practical tool bridging academia and industry deployment
97.59% accuracy with Random Forest on CWRU benchmark dataset
Interactive Streamlit dashboard for live inference & demo
FUTURE SCOPE
Validate on additional industrial real-world datasets
Extend to XGBoost, 1D-CNN for higher accuracy
Fault severity estimation and remaining useful life (RUL)
Deployment on edge computing IoT devices
Thank You for Your Attention!
Pradeep Modak & Ashwini Kumar | Dept. of Mechanical Engineering, NIT Jamshedpur | April 2026

## Slide 14
REFERENCES
1.Case Western Reserve University Bearing Data Center, Bearing vibration data repository,https://engineering.case.edu/bearingdatacenter
2 P. K. Kankar, S. C. Sharma, S. P. Harsha, Fault diagnosis of ball bearings using machine learning methods, Expert Systems with Applications, 2011 https://www.researchgate.net/publication/220220016_Fault_diagnosis_of_ball_bearings_using_machine_learning_methods
3 C. S. Rajeswari, S. Sathiyabama, S. Devendiran, Bearing fault diagnosis using wavelet packet transform, hybrid PSO and support vector machine, Procedia Engineering, 2014. https://www.researchgate.net/publication/275540896_Bearing_Fault_Diagnosis_using_Wavelet_Packet_Transform_Hybrid_PSO_and_Support_Vector_Machine
4. Streamlit documentation https://docs.streamlit.io/

## Slide 15
Thank You
Questions & Discussion
Ashwini Kumar (2023UGCM004) | Pradeep Modak (2023UGCM026)
Supervisors: Dr. Saroj Kumar Sarangi | Dr. Abhijit Dey
NIT Jamshedpur · Dept. of Mechanical Engineering · April 2026